## Slide 1
Presentation of PIC Microcontroller
Question: How to design a circuit using PIC Microcontroller to control the stepper motor by generating following pattern:
1100 , 0110 , 0011, 1001
intro

## Slide 2
Presentation of PIC Microcontroller
Question: How to design a circuit using PIC Microcontroller to control the stepper motor?
intro
contents
01
02
03
Naiha Rafiq
BS ELE 5TH SEMESTER
For Introduction
M.Waleed
BS ELE 5TH SEMESTER
For Explanation
Saleem Raza
BS ELE 5TH SEMESTER
For Programming and
Result

## Slide 3
Presentation of PIC Microcontroller
Question: How to design a circuit using PIC Microcontroller to control the stepper motor?
about
contents
PIC 18
What is PIC 18 and
What is Stepper motor
Applications of
Stepper motor
Motor diagram &
Circuit diagram
C programming
& Results
Types of Stepper motor:
Unipolar and Bipolar
Types of modes of Unipolar

## Slide 4
Presentation of PIC Microcontroller
Question: How to design a circuit using PIC Microcontroller to control the stepper motor?
about
history
PIC 18
Stepper motor
PIC microcontrollers are a family of specialized microcontroller
chips produced by Microchip Technology in Chandler, Arizona.
The acronym PIC stands for "peripheral interface controller."
A Typical microcontroller includes a processor, memory, and peripherals.

## Slide 5
Presentation of PIC Microcontroller
Question: How to design a circuit using PIC Microcontroller to control the stepper motor?
about
history
timeline
Stepper motor
applications
Stepper motor
A stepper motor, also known as step motor or stepping motor, is a brushless DC electric motor that divides a full rotation into a number of discrete steps.

## Slide 6
Presentation of PIC Microcontroller
Question: How to design a circuit using PIC Microcontroller to control the stepper motor?
about
history
timeline
teams
working
applications
Working of stepper motor:
The stepper motor uses the theory of operation for magnets to make the motor shaft turn a precise distance when a pulse of electricity is provided. The stator has eight poles, and the rotor has six poles. The rotor will require 24 pulses of electricity to move the 24 steps to make one complete revolution.

## Slide 7
Presentation of PIC Microcontroller
Question: How to design a circuit using PIC Microcontroller to control the stepper motor?
about
history
timeline
teams
services
applications
types
Applications of stepper motor
stepper motors are used in:
floppy disk drives,
computer printers,
plotters,
slot machines,
image scanners,
compact disc drives,
and, more recently, in 3D printers.

## Slide 8
Presentation of PIC Microcontroller
Question: How to design a circuit using PIC Microcontroller to control the stepper motor?
about
history
timeline
teams
services
follow
types
Further explanation
unipolar
bipolar
In the unipolar stepper motor which works with one winding with a center tap per phase, each section of the phase winding is turned on for each of the magnetic field direction. Since unipolar stepper motors are quite easy to operate, these are highly preferred among hobbyists.
In a bipolar stepper motor, there is a single winding per phase. This makes the driver circuit lot more complicated while reversing the magnetic poles which in turn reverses the current in the winding.

## Slide 9
Presentation of PIC Microcontroller
Question: How to design a circuit using PIC Microcontroller to control the stepper motor?
about
history
timeline
teams
services
follow
about
Further explanation
C diagram
Full step
In full step operation each step has a movement of 1.8 degrees and hence it takes 200 steps to complete a full revolution. This is made possible by energizing either single of stator winding or two phases. Since the two phases are energized at the same time in the dual phase operation, torque and speed are greater in this kind of operation while the single phase operation requires a lower amount of power from the driver circuit.

## Slide 10
Presentation of PIC Microcontroller
Question: How to design a circuit using PIC Microcontroller to control the stepper motor?
about
history
timeline
teams
services
follow
about
history
c. diagram
C program

## Slide 11
Presentation of PIC Microcontroller
Question: How to design a circuit using PIC Microcontroller to control the stepper motor?
about
history
timeline
teams
services
follow
about
history
timeline
C program
output
C Program:
#include<xc.h>
#define PC0 PORTCbits.RC0
#define PC1 PORTCbits.RC1
#define PC2 PORTCbits.RC2
#define PC3 PORTCbits.RC3
void main (void)
{
unsigned char conbyte = 0xC;
unsigned char conbyt = 0x6;
unsigned char conby = 0x3;
unsigned char conb = 0x9;
unsigned char regALSB;
unsigned char regALS;
unsigned char regAL;
unsigned char regA;
unsigned char x;
regALSB=conbyte;
regALS=conbyt;
regAL=conby;
regA=conb;
TRISCbits.TRISC0=0;
TRISCbits.TRISC1=0;
TRISCbits.TRISC2=0;
TRISCbits.TRISC3=0;
for(x=0; x<4; x++)
{
PC0 = regALSB & 0x01;
regALSB = regALSB >> 1;
PC1 = regALS & 0x01;
regALS = regALS >> 1;
PC2 = regAL & 0x01;
regAL = regAL >> 1;
PC3 = regA & 0x01;
regA = regA >> 1;
}
}

## Slide 12
Presentation of PIC Microcontroller
Question: How to design a circuit using PIC Microcontroller to control the stepper motor?
about
history
timeline
teams
services
follow
about
history
timeline
teams
output
The end

## Slide 13
Presentation of PIC Microcontroller
Question: How to design a circuit using PIC Microcontroller to control the stepper motor?
THE END
Thank You
The End